## Slide 1
SMART ELEVATOR SYSTEM
9-Floor Elevator Control Using ATmega32
Embedded Systems Simulation Project • Proteus ISIS
Team
Youssef Alaa • Mostafa Ahmed • Habiba Mohamed • Youmna Tamer • Madonna

## Slide 2
Project Overview
The Smart Elevator System is a 9-floor elevator controller built around the ATmega32 microcontroller and simulated in Proteus. Users request a floor using keypad, and the system automatically works out the direction of travel, moves the elevator, and manages the door while an LCD keeps the passenger informed at every step.
Floor selection via keypad
Automatic direction decision (UP / DOWN)
Live LCD status and system messages
Automatic door open / close timing
Emergency stop with alarm
Current Floor
Floor 9
Floor 8
Floor 7
Floor 6
Floor 5
Floor 4
Floor 3
Floor 2
Floor 1

## Slide 3
Objectives
Automate Control Logic
Handle floor requests and decide travel direction without manual intervention.
Real-Time Status Display
Show current floor, direction, and door state on the LCD at all times.
Guarantee Passenger Safety
Provide an immediate emergency stop with alarm and warning message.
Realistic Hardware Simulation
Model motor movement, servo-driven doors, and indicators inside Proteus.

## Slide 4
System Architecture
ATmega32
Main Controller
Keypad
Emergency Button
DC Motor (via L293D)
Servo Motor (Door)
LCD Display
Status LEDs
Buzzer
Inputs
Outputs

## Slide 5
Hardware Components
ATmega32
Main controller running the elevator logic
LCD
Displays floor, direction, door status, messages
Keypad
Used to select the desired floor
DC Motor
Simulates upward and downward movement
L293D Driver
Controls the direction of the DC motor
Servo Motor
Simulates opening and closing the door
LEDS
LED(G) : indicate to normal state
LED(R) : Indicate to emergency state
Buzzer
Sounds an alarm during emergencies
Emergency Button
Immediately triggers an emergency stop

## Slide 6
Software / Driver Modules
DIO
Buttons, motor control lines, LEDs, and buzzer
EXTI + GIE
External interrupt for the emergency button
TIMER
Movement timing, door timing, and servo
LCD Driver
Displays elevator information
Keypad Driver
Reads floor selection input
LED Driver
status indication

## Slide 7
Operation Workflow
1
Select
Floor
2
Determine
Direction
3
Move
Elevator
4
Arrive &
Stop
5
Open
Door
6
Wait
7
Close
Door
8
Ready for
Next Request
The controller repeats this cycle for every new floor request, choosing the shortest and most efficient path based on the elevator's current position and direction.

## Slide 8
Display & Status Indicators
Moving Up
Floor: 1
16x2 LCD • Live System Status
LCD Shows
Current floor number
Movement direction (UP / DOWN)
Door status (OPEN / CLOSED)
System and emergency messages
LED Indicators
LED(G) : indicate to normal state
LED(R) : Indicate to emergency state

## Slide 9
Automatic Door Control Servo + Timer0
Timer0 runs in CTC mode to generate a steady 100 µs interrupt (OCR0 = 99, prescaler = 8)
A software tick counter counts these 100 µs interrupts to time each phase precisely
A state machine drives the pin: IDLE → PULSE_HIGH → PULSE_LOW → IDLE
1 ms HIGH (10 ticks) = 0° → door CLOSED • 1.5 ms HIGH (15 ticks) = 90° → door OPEN
The LOW phase automatically completes the ~20 ms (200-tick) frame
Servo Control Signal
Built from 100 µs Timer0 ticks (CTC, OCR0 = 99)
0° (CLOSE)
HIGH = 1 ms
1 ms
19 ms
90° (OPEN)
HIGH = 1.5 ms
1.5 ms
18.5 ms
Period ≈ 20 ms frame • 200 × 100 µs ticks — LOW time completes the frame automatically

## Slide 10
Emergency Safety System
A dedicated emergency button is wired to the ATmega32's external interrupt (EXTI) with Global Interrupt Enable (GIE) active, so it can react the instant it is pressed — regardless of what the controller is currently doing.
Elevator motion stops immediately
Alarm buzzer is activated
LCD displays an emergency message

## Slide 11
Additional Features
Multiple Floor Requests
Queue and serve several requested floors in one trip
Direction-Based Priority
Serve requests in the order that matches current travel direction
Door Closing Countdown
Display a countdown before automatically closing the door
Door Obstruction Detection
Detects blockage and re-opens the door for safety
Overload Warning
Warns when the cabin exceeds its safe weight limit

## Slide 12
Thank You
A safe, automated, and realistic 9-floor elevator control system built around the ATmega32.
GitHub Repository